## Slide 1
Water quality-Graphical presentation-Statistical methods
Aristotle University of Thessaloniki

## Slide 2
The geological formations through which the water has flow can be traced from its quality characteristics. The main processes that take place during water flow are dissolution, oxidation-reduction, ionic exchange-adsorption-absorption.
Surface and groundwater quality depends on the following factors:
Composition of the geological formations since water interacts with the environment
Residence time of the water in the subsurface (thereafter velocity and hydraulic conductivity are determining factors for groundwater)
-Temperature
-The initial chemical composition of the rainwater
- Organic materials (production CO2, reduction Fe, NO3, SO4, CH4)
- Vegetation (absorption K, P, gases from atmosphere etc)
-Redox, chemical and ion-exchange actions (ie it depends on the prevailing process)
- Human activities (use of fertilizers and pesticides, wastewater disposal, industrial activity e.t.c.)
Surface and Groundwater Quality Characteristics

## Slide 3
Sources of water constituents:
Ca: calcite, dolomite
Mg: dolomite, olivine
Na: halite (NaCl), feldspars (albite), industrial wastes
K: clay minerals, seawater intrusion
NO3: agricultural activities (fertilizers)
SO4: Oxidation of sulfide ores, gypsum
Fe: igneous rocks, ferrous sulfide (FeS2)
Mn: metamorphic rocks, mica biotite
Cl: seawater intrusion, industrial wastes
HCO3, CO3: limestone, dolomite
Surface and Groundwater Quality Characteristics

## Slide 4
Typical composition of groundwater samples according to the geological formation:
Karstic water: increased value of HCO3. Limestone water are rich in Ca and dolomitic in Mg.
Ophiolitic water: Mg and SO4 are the prevailing ions
Water from granitic rocks: increased values of Na and K are recorded (they are not the prevailing ions but higher values than typical are observed). The total dissolved solids value are low. High values of Sr, Al, Li are also detected
Water from alluvial formations: the main cation is Ca and the main anion HCO3. High values of total dissolved solids and electrical conductivity is the mai characteristic of this water type.
Gneiss and schist water: low total dissolved solids and electrical conductivity values. They have relatively K,Na, Cl values.
Phyllite rocks water: high values of Fe and Mn. Relatively high vale of SO4.
Surface and Groundwater Quality Characteristics

## Slide 5: The results of groundwater samples chemical analyses can be presented in tables. This type of presentation is not always convenient for scientists to interprete and manage these data. Therefore, over time many graphical ways for the presentation of hydrochmical data were developed. These methods allowed scientists to compare samples, to detect origin of water, residence time, mixing of water, to clasify or to characterize samples regarding their use, in a very short time. The graphical methods provide also a statistical process of the data. Graphical presentations give a better understanding of the natural processes that take place in an area and there fore can be used as a usefull tool in the design of an integrated resources management plan
The most common ways for presentation of water samples chemical analyses are the following:
Hydrochemical maps and sections
Hydrochemical time diagrams
Correlation graphs
Hydrochemical diagrams
Ionic ratios
Surface and groundwater classification
Presentation of hydrochemical data
Selected indicative methods for the presentation of hydrochemical data are following to the next slides

## Slide 6: Hydrochemical maps
Spatial distribution of EC (μS/cm)
Spatial distribution of Ca (mg/lt)
The spatial distribution of the values of a parameter are depicted with contours on a map giving the ability to the researcher to delineate groundwater contamination and to compare maps from different time periods.

## Slide 7: Hydrochemical sections
Hydrochemical section orientation
Groundwater flow direction
The hydrochemical section should be designed along the groundwater flow

## Slide 8: Hydrochemical section
Enrichment of groundwater in Na is detected at a distance of approximately 30 km from the begining point indicating a change in the hydrogeological conditions or pollution from human activities in this area
In a section the parameter values versus distance
are designed.
Distance
Hydrochemical section AB of Na (mg/l)

## Slide 9: Hydrochemical section (surface water)
Sections of the branches of a hydrographic network are shown on the figures depicting the enrichment in na, Cl and the increase of electrical conductivity due to the mineral dissolution from the rocks along flow

## Slide 10
Hydrochemical diagrams
Fluctuation of the Mg concentration from a water sample over time
Correlation of the river discharge (l/sec) and the Mg concentration values of a surface water sample

## Slide 11
Statistical Processing
Linear Regression
The most simple way to present in a graphical way the correlation of two parameters. The statistically significant correlation between the two parameters could indicate possible common origin (seawater intrusion for example in the figure above)
Correlation of Na versus Cl

## Slide 12
Hydrochemical diagrams
Bar diagrams
Source: https://www.slideshare.net/naarakshashi/graphical-presentation-and-classification-for-assessment-of-ground-water-quality-by-ism-ravi-kiran-jp
http://inside.mines.edu/~epoeter/_GW/18WaterChem2/WaterChem2pdf.pdf
Display of concentrations (not ratios) for individual samples but as it is a cumulative chart the values are not readily apparent
Total height ~ reflects TDS
Easier to compare samples than pie charts

## Slide 13
Hydrochemical diagrams
Radius-polygonic diagrams

## Slide 14
Hydrochemical diagrams
Sector diagrams
Display of concentration ratios for individual samples
Easier to compare concentration ratios for several different samples compared with a table of numbers
Source: http://inside.mines.edu/~epoeter/_GW/18WaterChem2/WaterChem2pdf.pdf

## Slide 15
Horizontal polygonic diagramms
Hydrochemical diagrams
Displays concentration ratios for individual samples. Shape makes it easier to compare samples. Especially if displayed on maps

## Slide 16
ADVANTAGES
Visualizes the samples that are ionically related and the flow path can be detected
When the groundwater flow path is known, the diagram can be used to show the change in chemical composition over time or space
DISADVANTAGES
One sample per diagram can be illustrated
Hydrochemical diagrams
Horizontal polygonic diagramms
Source: https://www.slideshare.net/naarakshashi/graphical-presentation-and-classification-for-assessment-of-ground-water-quality-by-ism-ravi-kiran-jp

## Slide 17
Semi-loarithmic Schoeler diagram
Hydrochemical diagrams
Logarithmic diagrams of major ion analyses in meq/l demonstrate different water types on the same diagram
Sample concentrations not ratios are displayed and compared
Similar waters exhibit similar fingerprints
Source: http://inside.mines.edu/~epoeter/_GW/18WaterChem2/WaterChem2pdf.pdf

## Slide 18
Classification according to Piper diagram
Hydrochemical diagrams
The Piper plot classifies water samples in hydrochmeical facies. It is the most common diagram used in the field of hydrogeology

## Slide 19
Hydrochemical diagrams
Classification according to Piper diagram
The percentage of the ions and cations (seperately) are calculated as it is shown on the Table

## Slide 20
Hydrochemical diagrams
Classification according to Piper diagram
The percentage of the cations is illustrated in the cations triangular plot

## Slide 21
Hydrochemical diagrams
Classification according to Piper diagram
The percentage of the anions is illustrated in the anions triangular plot

## Slide 22
Hydrochemical diagrams
Classification according to Piper diagram
The two previous projections of the anions and cations are projected in the upper diamond shaped field for the classification of the sample

## Slide 23
Piper classification
Advantages
Many samples are depicted in the same diagram
It can be used for the detection of water mixing
Spatial and temporal changes in the chemical composition of the samples can be detected
Disadvantages
Piper diagram is not suitable for water samples that have high concentration values of ions that do not participate in the diagram
Hydrochemical diagrams

## Slide 24
Durov classification
Hydrochemical diagrams
Source: Salman, S.A., Melegy, A.A., Shaban, A.M. and Hassaan, M.M. (2013). Hydrogeochemical Characteristics and classification of Groundwater in Sohag Governorate, Egypt. Journal of Applied Sciences Research, 9(1): 758-769, ISSN 1819-544X

## Slide 25
S.A.R. classification
Hydrochemical diagrams
Sodium adsorption ratio (SAR) is a measure of the suitability of water for use in agricultural irrigation, as determined by the concentrations of solids dissolved in the water. It is also a measure of the sodicity of soil, as determined from analysis of water extracted from the soil. The formula for the calculation of S.A.R is given below:

## Slide 26
Wilcox classification
Concentrations are expressed in meq/l
Hydrochemical diagrams
Wilcox diagram investigates the suitability of water for irrigation purposes

## Slide 27
Chernoff faces
Hydrochemical diagrams

## Slide 28
Groundwater quality characteristics are strongly determined by hydrogeological processes regarding the environment, the flow properties (velocity, hydraulic conductivity), the physicochemical parameters (e.g. temperature) and the anthropogenic activities. The graphical presentation techniques that have been developed can not detect the relationship between the different parameters (variables) or between the samples and the fact that only specific parameters can be depicted.
Statistical methods allow the grouping of samples or parameters separating samples of different origin or different types. They also enable the delineation of areas with different groundwater quality characteristics after the spatial distribution of the results (e.g. Factor or cluster analysis). Polluted areas can be detected. The relationship between the parameters can reveal the possible pollution source in an area.
In the following slides statistical methods are presented. Emphasis is given in multivariate methods such as factor and cluster analysis
Statistical methods

## Slide 29
Statistical methods
Correlation Analysis
Correlation coefficient (Pearson) is a statistical tool to show the degree of dependency of one variable with the other. It is commonly used to measure and establish the relationship between two variables (Batabyal 2014).
r=
where cov(X,Ψ)=Σni=1 (xi-xm) (ψi-ψm)
σχ, σψ= standard deviations of Χ and Ψ respectively
xm,ψm= mean values of Χ and Ψ
The Pearson coefficient values range between -1 to 1

## Slide 30
Correlation Analysis
Significant correlation between Na-Cl
Statistical methods

## Slide 31
Three main types of correlation have been recognized in the water systems
There is a strong competative relationship between ions with the same charge but different valance
A strong linear relationship between ions with opposite charge and same valance
A non competative relationship between ions with the same kind of charge and same valance
Statistical methods

## Slide 32
Multiple Linear Regression
The linear equation is used
The R2 coefficient is used to check the statistical significance of the equation. This coefficient shows the percentage of the dispersion of the data that this equations describe
The F ratio must be statistically significant in comparison to the crucial value (Fm,n) which is given from Tables
The parameters that participate in the equation are strongly correlated between them
Statistical methods
Multiple Linear Regression method provides equation linking of a dependent variable to the independent variable (Chenini and Khemiri; 2009)

## Slide 33
Multiple Linear Regression
EC=73.9+2.8 Ca+9.1 Mg+4.3 Na+0.26 Cl
R= 0.963
R2 =0.927 the 92.7% of the dispersion is described by the equation
The F ratio value is 192.6, which is significantly larger from the crucial value (it is equal to 4.1, given from Tables)
Statistical methods

## Slide 34
R-Factor Analysis
Statistical methods
The R-factor analysis is a data reduction method. A large number of interdependent variables can be described by a small number of factors (latent variable) that represent to a significant degree the initial variables (Voudouris et al., 1997, 2000). This method contributes to the simplification of complex problems that are described by many parameters, without losing information (Qian et al 1994). The factors that describe the interdependent variables are functionally independent and they behave in the same way with the statistically significant variables that participate in the factors (Anazawa and Ohmori, 2005, Brown, 1998). For the simplification of the procedure a varimax rotation is conducted in order to reduce the number of factors that describe the total variance (Mathes et al., 2006, Mencio and Mas-Pla, 2008). Usually, the factors that are finally selected are those that show eigenvalue higher than one (Cattell, 1978). The number of the factors that will result could be indicative of the reasons that cause the data variation (Sandow et al., 2008). Each factor describes a specific hydrogeological process, depending on the participating variables. The factor scores can be calculated for each sampling point and reveal the effect of the factor at the specific location. They can be used to draw contour maps that depict the spatial distribution of the factors. Negative scores represent areas that are not affected by the process that the factor describes. On the contrary, positive or near zero scores, represent areas that are affected by the factor.
Source: Ch. Mattas, M. Papachristou (2014). ASSESMENT OF GROUNDWATER QUALITY CHARACTERISTICS FROM THE UPPER PART OF GALLIKOS RIVER BASIN (N. GREECE) USING FACTOR AND CLUSTER ANALYSIS METHODS. Proceedings: 10th International Hydrogeological Congress of Greece / Thessaloniki, 2014, p. 467-476

## Slide 35
R-Factor Analysis
Statistical methods
Component | Initial Eigenvalues |  |  |  | Factors |  | 
 | Total | % of Variance | Cumulative% |  | 1 | 2 | 3
1 | 4,663 | 46,631 | 46,631 | Cl | 0,95 | 0,166 | 0,026
2 | 2,036 | 20,363 | 66,994 | NO3 | 0,054 | 0,579 | 0,709
3 | 1,092 | 10,916 | 77,91 | SO4 | 0,489 | 0,377 | -0,221
4 | 0,733 | 7,33 | 85,24 | HCO3 | 0,137 | 0,796 | 0,086
5 | 0,498 | 4,983 | 90,223 | K | -0,227 | 0,282 | 0,807
6 | 0,458 | 4,579 | 94,802 | Na | 0,921 | 0,076 | 0,023
7 | 0,255 | 2,554 | 97,356 | Mg | 0,561 | 0,650 | 0,071
8 | 0,193 | 1,925 | 99,281 | Ca | 0,527 | 0,702 | 0,124
9 | 0,049 | 0,492 | 99,773 | EC | 0,830 | 0,496 | 0,092
10 | 0,023 | 0,227 | 100 | pH | 0,228 | -0,245 | 0,842

## Slide 36
R-Factor Analysis
Eigenvalues and factors plot
Statistical methods

## Slide 37
R-Factor Analysis
Statistical methods
Factor 1 interprets 45.23% of the variance. Chlorides, Sodium and Electrical Conductivity participate in this factor. These variables are associated to the impact of the anthropogenic activities on groundwater.

## Slide 38
Cluster Analysis
The cluster analysis aims at grouping the hydrochemical parameters and the water samples according to their similarities so that each group represents a specific hydrochemistry process in the study area
There are two types of cluster analysis, the hierrachical cluster and the (K-means cluster
Statistical methods
Hierarchical cluster is a very efficient tools in analyzing water-chemistry data and identifying the factors that affect its chemical composition

## Slide 39
Analyze Classify Hierarchical Cluster
Cluster Analysis
Statistical methods
SPSS software can be used for the implementation of cluster analysis following the next steps

## Slide 40
Cluster Analysis
The use of this window will vary substantially depending on whether you choose to Cluster Cases or to Cluster Variables. The example on the left figure focuses on Clustering Cases. To cluster cases you need to identify variables you wish to be considered in creating clusters for the cases. Pass these in the Variable(s) box. Then you need to specify how you wish your cases to be identified. This will usually be an ID number or some identifying name (here the variable brand). See the right figure above.
Statistical methods

## Slide 41
Cluster Analysis
None: All clusters are listed since all possible solutions will be identified. What it does not do is identify cases included in each cluster for a particular solution
Single solution:Specify some number greater than 1 that indicates cluster membership for a specific number of clusters. For instance if you type 3 into the box indicating number of clusters, SPSS will print out a 3-cluster solution.
Range of solutions: If you wish to see several possible solutions, type the value for the smallest number of clusters in the first box and the value for largest number of clusters you wish to see in the second box. For instance if you type in 3 and 5, SPSS would show case membership for a 3-cluster, a 4-cluster and a 5-cluster solution.
Determination of the number of clusters
Statistical methods

## Slide 42
Cluster Analysis
Plots: An icicle plot of the entire clustering process is included by default. The Dendrogram provides information similar to that covered in the icicle plot but features, in addition, a relative measure of the magnitude of differences between variables or clusters at each step of the process.
Statistical methods

## Slide 43
(Cluster Analysis)
Cluster Method: Choose the procedure for combining clusters. SPSS computes the smallest average distance between all group pairs and combines the two groups that are closest
Measure: Indicate what method is used for distance measuring, the default is Squared Euclidean distance.
Transform values: The solution suggested by SPSS is to standardize all variables – for example, change each variable to a z-score (with a mean of 0 and a standard deviation of 1). This will give each variable equal metrics, but will give them equal weight as well.
Statistical methods

## Slide 44
Cluster Analysis
One of the following methods can be selected for the implementation of cluster analysis regarding the shaping of the groups
furthest neighbour
nearest neighbour
between groups-linkage
within groups linkage)
median clustering
centroid clustering
Ward method
Statistical methods

## Slide 45
Cluster Analysis
At Stage 1, Case 1 is clustered with Case 3. The squared Euclidean distance between these two cases is .002. Neither variable has been previously clustered (the two zeros under Cluster 1 and Cluster 2), and the next stage (when the cluster containing Case 1 combines with another case) is Stage 17. (Note that at Stage 17, Case 2 joins the Case-1 cluster.)
Statistical methods

## Slide 46
Cluster Analysis
Statistical methods
At Stage 10, Case 9 joins the Case-11 cluster (Case 11 was previously clustered with Case 14 back in Stage 5, thus creating a cluster of 3 cases: Cases 9, 11, and 14). The squared Euclidean distance between Case 9 and Case-11 cluster is 19.833. Case 9 has not been previously clustered (the zero under Cluster 1), and Case 11 was previously clustered at Stage 5. The next stage (when the cluster containing Case 9 clusters) is Stage 15 (when it combines with the Case-6 cluster).

## Slide 47
Cluster Analysis
At Stage 14, the clusters containing Cases 12 and 19 are joined, Case 12 has been previously clustered with Case 17, and Case 19 had been previously clustered with Cases 20 and 21, thus forming a cluster of 5 cases (Cases 12, 17, 19, 20, 21). The squared Euclidean distance between the two joined clusters is 31.667. Case 12 was previously joined at Stage 3 with Case 17. Case 19 was previously joined at Stage 7 with the Case-20 cluster. The next stage when the Case-12 cluster will combine with another case/cluster is Stage 16 (when it joins with the Case-10 cluster).
Statistical methods

## Slide 48
Cluster Analysis
Statistical methods
The branching-type nature of the Dendrogram allows you to trace backward or forward to any individual case or cluster at any level. It, in addition, gives an idea of how great the distance was between cases or groups that are clustered in a particular step, using a 0 to 25 scale along the top of the chart. While it is difficult to interpret distance in the early clustering phases (the extreme left of the graph), as you move to the right relative distance become more apparent. The bigger the distances before two clusters are joined, the bigger the differences in these clusters. To find a membership of a particular cluster simply trace backwards down the branches to the name.

## Slide 49
Cluster Analysis
Statistical methods

## Slide 50
Cluster Analysis
Phenon line
Statistical methods
The phenon line cuts the structure at a chosen level.
The cluster analysis of variables defines four associations at the phenon line:
The first (Mg2+, Ca2+, SO42-) indicates the dissolution of gypsum and/or anhydrite; the second (Na+, Cl, K+) suggests evaporite weathering, possibly halite and sylvite; the third (SiO2) indicates silicate weathering; and the fourth (HCO3 , NO3) indicates important calcite weathering processes related to gypsum weathering processes

## Slide 51
Cluster Analysis
The aim of K-means (or clustering) is this : to group the items into k clusters such that all items in same cluster are as similar to each other as possible and items not in same cluster are as different as possible. The distance measures to calculate similarity and dissimilarity are used. One of the important concept in K-means is that of centroid. Each cluster has a centroid. You can consider it as the point that is most representative of the cluster. Equivalently, centroid is point that is the "center" of a cluster. Simply speaking it is an algorithm to classify or to group your objects based on attributes/features into K number of group. K is positive integer number. The grouping is done by minimizing the sum of squares of distances between data and the corresponding cluster centroid . Thus, the purpose of K-mean clustering is to classify the data.
Statistical methods
Mohammad M. Faqe Hussain, Akhterkhan S.Hamad (2012). Use K-Means Cluster Analysis to Study the Classification Of Some Water Factories, According To Some Specifications On The Cover Of The Bottle. IOSR Journal of Engineering (IOSRJEN) ISSN: 2250-3021 Volume 2, Issue 8 (August 2012), PP 29-37

## Slide 52
Mohammad M. Faqe Hussain, Akhterkhan S.Hamad (2012). Use K-Means Cluster Analysis to Study the Classification Of Some Water Factories, According To Some Specifications On The Cover Of The Bottle. IOSR Journal of Engineering (IOSRJEN) ISSN: 2250-3021 Volume 2, Issue 8 (August 2012), PP 29-37
Cluster Analysis
Statistical methods
The basic step of k-means clustering is simple. In the beginning, we determine number of cluster K and we assume the centroid or center of these clusters. We can take any random objects as the initial centroids or the first K objects can also serve as the initial centroids. Then the K means algorithm will do the three steps below until convergence Iterate until stable (= no object move group): 1. Determine the centroid coordinate 2. Determine the distance of each object to the centroids 3. Group the object based on minimum distance (find the closest centroid)

## Slide 53
Steps for the implementation of K-means method using SPSS software
Analyze→Classify→K-Means Cluster
Cluster→ Variablesκαι τις εισάγω στο πλαίσιο
Numbers of Clusters→select the number of clusters
Method→classify only
Save→ cluster membership
Options→Initial cluster centers
Cluster Analysis
Statistical methods

## Slide 54
Cluster Analysis
Statistical methods
Cluster 1: samples polluted due to human activities (example from Gallikos river basin, Greece)

## Slide 55
Cluster Analysis using K-means method
Statistical methods
The cluster analysis seperates the polluted (from human activities) samples