## Slide 1
Methodologies Contributing to Water Resources Management (DPSIR and DRASTIC methods)
Aristotle University of Thessaloniki

## Slide 2
DPSIR
The Driver–Pressure–State–Impact-Response (DPSIR) framework for integrated environmental reporting and assessment, developed by the European Environmental Agency (EEA) in 1999, has since been widely adopted. According to the DPSIR framework there is a chain of causal links starting with ‘driving forces’ (economic sectors, human activities) through ‘pressures’ (emissions, waste) to ‘states’ (physical, chemical and biological ) and ‘impacts’ on ecosystems , human health and functions, eventually leading to political ‘responses’ (prioritisation, target setting, indicators).
• Driving forces (or Drivers) refer to fundamental social processes, such as the distribution of wealth, which shape the human activities that have a direct impact on the environment.
• Pressures are both the specific human activities that result from driving forces which impact the environment, such as the resource extraction necessary to fuel the automobile fleet of the United States, and the natural processes that have a similar impact on the environment, such as volcanoes and solar radiation.
• State is the condition of the environment. This condition, under current conceptualizations, is not static, but is meant to reflect current environmental trends as well.
• Impacts are the ways in which changes in state influence human well-being.
• Responses generally refer to institutional efforts to address changes in state, as prioritized by impacts.
Source: Carr, E.,Wingard, P., Yorty, S., Thompson, M., Jensen, N., Roberson, J. Applying DPSIR to sustainable development. International Journal of Sustainable Development & World Ecology 14, 2007, 543–555.

## Slide 3
The widely used Driver-Pressure-State-Impact-Response (DPSIR) analytical framework has been adapted to the definitions given in Groundwater Risk Assessment; Technical report developed on the basis of the Guidance Document 2004, No. 3 ; as follows:
− Driver: An anthropogenic activity that may have an environmental effect. Drivers produce a series of pressures and are quantified by aggregated data, e.g., population density, hectares of irrigated land, industrial units etc.
− Pressure: The direct effect of the driver. Pressures form the manifestation of the effects the Driving Forces have on the water bodies. Pressures degrade the State of water bodies and have an Impact on them as well as on humans. Increased irrigation-industrial-domestic demands, precipitation decrease, point or non-point source pollution could be considered as pressures.
− State: The condition of the water body resulting from both natural and anthropogenic factors (e.g. chemical or ecological characteristics, water quantity, etc.).
− Impact: The effect upon human well being.
− Response: The measures taken to improve the state of the water body.
DPSIR

## Slide 4
DPSIR
Source: Kristensen, P. The DPSIR Framework. Paper presented at the 27-29 September workshop on a comprehensive/detailed assessment of the vulnerability of water resources to environmental change in Africa using river basin approach. 2004, UNEP Headquarters, Nairobi, Kenya.
Chain of causal links according to DPSIR framework

## Slide 5
DPSIR
The aim of managing water resources is to safeguard human health whilst maintaining sustainable aquatic and associated terrestrial ecosystems. It is, therefore, important to quantify and identify the current state of, and impacts on, water environment and how these are changing with time. The DPSIR model can be used as an analytical framework for assessing water issues. A generic DPSIR framework for water is shown in the figure on the next slide
Source: Kristensen, P. The DPSIR Framework. Paper presented at the 27-29 September workshop on a comprehensive/detailed assessment of the vulnerability of water resources to environmental change in Africa using river basin approach. 2004, UNEP Headquarters, Nairobi, Kenya.

## Slide 6
DPSIR
Source: Kristensen, P. The DPSIR Framework. Paper presented at the 27-29 September workshop on a comprehensive/detailed assessment of the vulnerability of water resources to environmental change in Africa using river basin approach. 2004, UNEP Headquarters, Nairobi, Kenya.
A generic DPSIR framework for water

## Slide 7
DPSIR
A CASE STUDY FROM GALLIKOS RIVER BASIN, GREECE
The Gallikos River is located in northern Greece. The hydrological was measured at approximately 1050 km2. Most of the area lays at elevations of lower than 600 m whilst in the northeast its watershed boundary reaches an altitude of 1180 m. The mean altitude was calculated at 308.5 m.
The total length of the river is about 73 km. The river flow characteristics resemble both a river and a torrent. Maximum discharges occur during summer and have been estimated at 700 m3/s.
The mean annual precipitation and temperature over the basin is about 480 mm and 16.5 °C
Geologically, the Gallikos basin is filled with Quaternary and Tertiary sediments. The bedrock of the basin is formed of argillaceous schists, limestones to dolimites, quartzites and gneiss
Ch. Mattas, K. S. Voudouris , A. Panagopoulos (2014). Integrated Groundwater Resources Management Using the
DPSIR Approach in a GIS Environment: A Case Study from the Gallikos River Basin, North Greece. Water 2014, 6, 1043-1068; doi:10.3390/w6041043

## Slide 8
Location of Gallikos river basin

## Slide 9
DPSIR
Driving forces: Urbanization, intensive agriculture, industry—especially along the coastal part of the basin—and to a minor extent animal breeding along the mountainous region, form the main driving forces of the study area
Pressures: Thoughtless use of fertilizers leads to nitrate pollution and elevation of phosphorus compounds in both surface and ground waters. Water demands for irrigation combined with uneven rainfall distribution throughout the year is also a major pressure related to agricultural activities. The overpumping of boreholes leads to groundwater level drawdown resulting in a decrease of reserves. Pressure due to the industrial activities is expressed in terms of chemical pollution of predominantly surface waters, but also of ground waters due to existing hydraulic interactions. The majority of the industries do not have wastewater treatment plants and the river and aquifers are the direct receptors of their effluents.

## Slide 10
DPSIR
State:
Surface Water: Surface water temperature ranges from 6.2 to 26 °C. Electrical conductivity ranges between 210 and 1760 μS/cm. In general, the composition of the surface water for cations is Ca2+ > Mg2+ > Na+ > K+. The composition of the surface water for anions is HCO3 − > Cl−. In the past years, several flood discharge events have occurred
Groundwater: High E.C. values are recorded in the Quaternary deposits aquifer. The groundwater quality of the karst aquifer is better than the other aquifers. The Ca(Mg)-HCO3 water type is the dominant type in the basin. Νitrate concentrations in excess of the threshold value of 37.5 mg/L, which is 75% of the maximum admissible concentration of 50 mg/L are documented on several occasions. The maximum admissible values for Na+ and Cl− are 200 mg/L and 250 mg/L, respectively. The threshold value is 150 mg/L for Na+ and 187.5 mg/L for Cl−. Exceedance of the maximum admissible values was recorded in the aquifer. High concentrations of Fe and Mn are recorded in the crystalline rocks and are attributed to the lithological composition of the area.

## Slide 11
DPSIR
Impacts: Within the study area, water is mainly used for domestic needs and for animal breeding and agriculture, the latter being by far the biggest consumer. Intensive and thoughtless fertilization results in aquifer pollution and renders groundwater improper for human consumption. Another side effect of the intensive agricultural practices is the overpumping that has as a result the reduction of the reserves. An increase of the karstic aquifer exploitation has been recorded in the recent years in order to cover the human consumption needs of the settlements.
Responses: Education of farmers on the implementation of European Laws and Directives on environmental protection and water resource management is a major issue. The importance of integrated water resources management is emphasized in the European Water Framework Directive (2000/60/EC). In response to this directive, Greek authorities have taken suitable initiatives to harmonize the Greek water policy. A comprehensive Code for Good Agricultural Practice (COGAP) has been compiled on the basis of the elaborated action plan for the wider study region. It addresses the effective reduction of nitrate groundwater pollution of agricultural origin through reduction and appropriate application of fertilization. The idea of reduction and appropriate application of fertilization sounds good in theory, but if it is not accompanied by financial incentives that will ensure the income of the farmers, such as subsidies, then it cannot be realistic. Recycled water potentially represents one important portion of the water resources for covering the increased water demands in the basin. Reuse of treated waste will be diverted for artificial recharge and recovered to be used for irrigation or industrial use.

## Slide 12
DPSIR

## Slide 13
The DRASTIC methodology a useful tool for the stakeholders and the decision makers, regarding the groundwater resources management. The DRASTIC methodology requires geological and hydrogeological data. The combination of the vulnerability index and the land use of the area, allows the estimation of the groundwater risk. The illustration of the spatial distribution of the vulnerability and risk assessment values, contributes to the effective design and the implementation of specific measures towards protection, restoration and integrated management of groundwater resources.
The model of DRASTIC estimates groundwater vulnerability and uses seven (7) parameters: Depth of groundwater, net Recharge, Aquifer media, Soil media, Topography, Impact of the vadose zone media, hydraulic Conductivity of the aquifer. The weight (w) of each parameter describes its significance, while the rating of the parameters indicates their participation and degree in the final vulnerability value for each point.
DRASTIC

## Slide 14
DRASTIC
The DRASTIC index (DI), where r is the rating for the study area and w is the importance weight for the parameter (Table 1). A numeric value assigned between 1 and 10 should have each parameter of the index, while the weight ranges from 1 to 5.
or DI=DrDw + RrRw + ArAw + SrSw + TrTw + IrIw + CrCw
The parameters of DRASTIC and their weight (Aller et al. 1987)
Source: Aller L, Bennett T, Lehr JH, Petty, RJ, Hackett G (1987). DRASTIC: A standardized system for evaluating ground water pollution potential using hydrogeologic settings. US Environmental Protection Agency, Report 600/2-85/018, Washington.
Mattas Ch., Kazakis N., Soulios G.: GROUNDWATER VULNERABILITY AND RISK ASSESSMENT USING DRASTIC MODEL IN A GIS ENVIRONMENT. A CASE STUDY FROM THE GALLIKOS RIVER BASIN, NORTHERN GREECE 10th International Hydrogeological Congress of Greece / Thessaloniki, 2014

## Slide 15
DRASTIC
The DRASTIC vulnerability index is indicative for the ease of which an external pollutant can reach an aquifer from the surface.
Source: Mattas Ch., Kazakis N., Soulios G.: GROUNDWATER VULNERABILITY AND RISK ASSESSMENT USING DRASTIC MODEL IN A GIS ENVIRONMENT. A CASE STUDY FROM THE GALLIKOS RIVER BASIN, NORTHERN GREECE 10th International Hydrogeological Congress of Greece / Thessaloniki, 2014
Vulnerability map according of the upper part of Gallikos river basin, Northern Greece

## Slide 16
DRASTIC
Source: Mattas Ch., Kazakis N., Soulios G.: GROUNDWATER VULNERABILITY AND RISK ASSESSMENT USING DRASTIC MODEL IN A GIS ENVIRONMENT. A CASE STUDY FROM THE GALLIKOS RIVER BASIN, NORTHERN GREECE 10th International Hydrogeological Congress of Greece / Thessaloniki, 2014
The groundwater risk map is the outcome of the combination of the vulnerability map (DRASTIC method) and the Hazard map (land uses) . There must be a pollution source in order to have pollution.
The land use map indirectly introduce the human activities in the risk assesment
The DRASTIC methodology can be used in order to design protection zones